All ideas and algorithms described in this article are the result of my independent and entirely self-sufficient intellectual activity. As the author, I give permission to freely use, modify and supplement all ideas and algorithms to any person or organization in any type of projects, subject to the obligatory reference to my authorship.

© Balyberdin Andrey Leonidovich 2019 Rutel.Nsk@Gmail.com

Synchronous Symbolic Hierarchy
Principles of Synchronous Channel Formation
(elimination of slippage effect)

Author: Balyberdin А.L.

Novosibirsk, 2022

 The transmission of voice traffic almost immediately switched to the synchronous channels (with a constant rate and transmission delay), and computer communications, up to now, are based on the “telegraph mode of communication” (Asynchronous Packet Switching). For the end user, a perfect network is one that provides precisely requested data transmission rate with pre-known and constant data transmission delay (my personal opinion). Synchronous (plesiochronous) networks have many disadvantages that prevent it from winning the competition against the packet switching. The proposed network, based on the principles of Synchronous Symbol Switching or Hierarchy (SSH), is a method of transparent transition of the computer networks to a synchronous mode of communication and is devoid of almost all the disadvantages intrinsic to such technologies as PDH. In a series of the articles, the principles of SSH operation will be described gradually and in sufficient detail to be a technical assignment for an electronic engineer.

Elimination of Slippage Effect

A synchronous mode of the data transmission has an unpleasant effect of losing or duplicating unit bits of the data being transmitted. It appears due to the lack of lockstep synchronization of the oscillators of all network transmitters (there are quite a lot of materials describing this problem and methods to combat it). PDH networks adopted complex and expensive methods to combat this phenomenon, which to a significant extent destroyed this technology along with the telephone industry using it (My opinion: It was destroyed by monopoly and negligence towards a consumer).

In almost all modern communication networks, a link level is synchronous. The transmitter is synchronized by its own oscillator, and the receiver restores the clock frequency from the data being received. The network section between such a transmitter and receiver can be considered as a synchronous data transmission channel. Transmission rates in the modern communication channels reach tens and hundreds of gigabits, with the switch frequency rates – at a few gigahertz. Therefore, a unit of transmission is not separate bits, but words (tens and hundreds of bits).
The data link layer fully complies with the requirements of the SSH and can be completely borrowed without modification or additional requirements.

Symbol Stream Level

The slippage effect is implemented in two options: as a skip and as an addition of an odd symbol. The option of skipping a symbol is the most “inconvenient” because it requires assessing to the transmitter. Sending symbols by the switch is slower than its receiving, which leads to the need in request for reduction of the rate to the previous switch, and it’s possible to recover lost data, but this can take a lot of time (which means it requires a buffer with a size which is unknown in advance). A large size buffer adds a long and variable delay, which is unacceptable to the end user (Requirement for Channel in SSH: Minimum and pre-known delay). The switch must be designed so that the switching time tends to four synchronization cycles (receiving a symbol, entry to the switch buffer, reading the switch buffer, transmitting a symbol). In the most optimal case, the switch buffer (switching matrix) must degenerate into a register storing one symbol.

It is necessary to create a mechanism that ensures that the symbol doubling option will be implemented (the switch input rate is less than the output rate) and to do this with minimal hardware and financial costs. The modern (budget) quartz crystal controlled oscillators have an accuracy at the level of 50 ppm (the discrepancy from the specified frequency does not exceed 50 parts per million); we believe that the mutual error is guaranteed not to exceed 500 ppm (as an example).

The simplest way to implement such a mechanism is to replace some of useful symbols in the user data stream with the “Compensating Symbols”. Usable stream rate will be reduced by 0.02%, but this is not a significant value.
In order to distinguish user symbols from the compensating ones, some kind of label is required, or one of the bit combinations must be reserved. Theoretically, it is possible to use service combinations of linear codes, but the absence of requirements for the link level was previously declared. In addition, this symbol is not the only one; further on, the whole tree circuit of various service symbols will be declared, including the user ones (transmitted data structuring).
Bit zero (the least significant bit of a symbol being transmitted) must indicate the type of a symbol. If it’s equal to zero - a user type, if one - a service type (interpreted by the switch).
I’ll immediately add that a bit equal to zero following the least significant one indicates that a symbol contains data; a bit equal to one contains a “signal”. The productivity (efficiency factor) of using a primary stream will not be affected (for a 100-bit symbol - 98%).

The mechanism for inserting compensating symbols must ensure a minimum buffer size. You cannot perform one-time insertion, for example 500 symbols once per second. The simplest and most effective way is to divide a second by the number of compensating symbols and add it evenly (at regular intervals) to the user data stream. In the course of this approach, the receiver buffer (in the ideal case) will always have exactly one symbol; the buffer will be empty or contain 2 symbols very rarely. When reading from an empty buffer, a compensating symbol should be read.
Positive effect: The delay due to the size of the switch buffer tends to the transmission time of one symbol in the stream.

Implementation example:
The transmitter generates synchronization and request signal to read the next symbol from FIFO switch. Between it and the switch, there is a block that once per preset number of clock cycles blocks the sampling of a symbol, and instead of it, inserts a compensating symbol (counter + multiplexer).
On the receiving side, when a compensating symbol is received, an entry to the switch FIFO is blocked.
The algorithm for eliminating slippage is quite transparent and does not require separate R&D. You can only compare the productivity (efficiency factor) of using a primary stream with existing network options.

My opinion: It will be even better than the packet switching, in which this mechanism is replaced with the need to transmit a preamble.