All ideas and algorithms described in this article are the result of my independent and entirely self-sufficient intellectual activity. As the author, I give permission to freely use, modify and supplement all ideas and algorithms to any person or organization in any type of projects, subject to the obligatory reference to my authorship.

© Balyberdin Andrey Leonidovich 2019 Rutel.Nsk@Gmail.com

Synchronous Symbolic Hierarchy
Industrial Automation Systems

Author: Balyberdin А.L.

Novosibirsk, 2022

Introduction.
Currently, the industrial automation systems use real-time operating systems that allow them to respond to signals received from the sensors within the specified time. To build complex APCSs, it is necessary to combine several control systems into a single network. APCS network must also meet certain sets of requirements, such as a delivery time guarantee, speed guarantee, and the ability to build backup channels, etc.

Currently, the vast majority of networks are the networks built on the principles of packet switching, and the packet switching cannot provide any guarantees on speed, losses and delivery. We can say that real-time systems exist, but real-time networks do not exist.
SSH network is built on the principles of the plesiochronous data stream switching and fully complies with the most stringent requirements of real-time systems.

What advantages can be obtained by introducing SSH network into the modern industrial automation systems?
Using the devices with SSH network interfaces as switches, you can create fully synchronous distributed data transmission systems with a guaranteed bandwidth and latency, independent of the network load with data from other devices. There is near-instant notification of failure of the communication lines or process controllers.

It is possible to add a small number of “extra” communication lines, so that it would be possible to build several independent connections between interacting devices. This will allow you to avoid losing data due to the local failures during the transmission process and build mechanisms to respond to such events.

If we go back in history of the development of electronic systems, previously electronics was significantly less reliable, and for obtaining the required quality of operation, there was used a complete multiple duplication with majority elements to identify errors. The modern controllers have become more reliable, compact, faster and, due to the high cost, have abandoned the use of this practice in most systems. The possibility of a new network allows it to be renewed without unnecessary financial costs, having received a significant reliability improvement of the control systems. Most controllers have performance that is many times greater than it is necessary to solve a specific problem, and it can be used to duplicate control programs. SSH network allows you to simultaneously transmit data to several recipients. These two properties allow you to run a copy of the same function on several physical controllers and control both the uniformity of data arrived via different routes, and the identity of operating results of the lower-level software.
On a real time basis, it is possible to duplicate critical parts of the control software, and when hardware failures are detected, to implement various types of corrective responses. The duplication process can be carried out at all levels of a control system. This mechanism must be implemented in the form of a standard library that automates most of the work of the system developer.
In addition, fairly simple mechanisms appear for debugging and saving the operating parameters of the system as a whole, linked to a real-time scale, but not for individual controllers as it is now.

The use of these mechanisms will make it possible to effectively create the control systems of extremely high reliability without using too much extra hardware.

Ways to implement SSH in the modern industrial automation systems.
A perfect solution for real-time systems would be a direct interface to SSH network (a network card or a module with this interface), but so far there are no such industrial controllers. To ensure that this problem does not slow down the implementation of SSH network, it is necessary to find a solution where SSH interface has only a switch, and all other equipment has only standard interfaces for microcontrollers and industrial computers (Ethernet, RS-485, CAN, etc.).

As an example, we will describe connecting a microcontroller via RS485 interface (half-duplex).
Since only a device with an implemented interface to SSH network has the property of delivery guarantee in real time, we select Master-Slave link type. The Master is a switch, or rather RS-485 modules implemented in the switch structure. The Slaves are all devices connected to these channels. The channel access algorithm is not very different from a canonical one; the Slave device gains access to a channel only after permission from the Master. SSH virtual channels have the property of transmitting symbols even if there is no transmission of real data, which ensures periodic sending of symbols towards the Slave devices. For uniformity, we add a mandatory response from the Slave device to the Master containing the data to be transmitted. If there is no response packet within the specified period, it is considered that this specific device is missing or has failed. The rest of the exchange rules will be formulated during the creation of a protocol.

An Approximate Algorithm for Data Exchange.

1. RS-485 module, as part of SSH switch, constantly monitors the state of FIFO virtual data channels intended for transmission to the Slave devices.
2. At the moment the data appears, an information packet is formed with the address of a specific device on an RS485 bus and data received from SSH network, with its further transmission via RS485 interface to the Slave device.
3. RS485 block on the Slave device receives a certain amount of data (packet header) and initiates the interrupt of a microcontroller to decode the packet header.
4. The interrupt handler checks whether a packet belongs to this device, and if an address matches, it begins to prepare a packet with response data (the data will be sent to SSH network).
5. Upon completion of receiving the incoming packet, the Slave device sends a response.

1. In its turn, SSH switch, after transmitting a packet, waits for a response. If there is no response for some time, a symbol, signaling about a communication error, is placed in the corresponding virtual channel (assigned to a given RS-485 address).
2. If a packet is received, the data from that packet is extracted and placed in a virtual channel buffer.