All ideas and algorithms described in this article are the result of my independent and entirely self-sufficient intellectual activity. As the author, I give permission to freely use, modify and supplement all ideas and algorithms to any person or organization in any type of projects, subject to the obligatory reference to my authorship.

© Balyberdin Andrey Leonidovich 2019 Rutel.Nsk@Gmail.com

Synchronous Symbolic Hierarchy
Operating Principles of Synchronous Stream Switch

Author: Balyberdin А.L.

Novosibirsk, 2022

Рисунок

Selection of Switch Structure.
Synchronous switches are quite simple in its design and represent small FIFOs connected in various ways (Clos networks, etc.); it is only a matter of the sizes of the switching field.
SSH was initially intended to achieve the maximum available transmission rates at low delays, which means that a “single-layer” switch will be the most optimal. Currently, the transmission rates have increased to such a level that there is a need to physically shorten the path between the source and receiver of the data.
If for the first IP data networks, the packet size in the cable (the path traveled by an electromagnetic wave during the data packet transmission) reached 150 km, and it didn’t matter in which area of the city to install the switch (except for cable savings), it was possible to lay “beautiful” wire bundles and create special areas for placing switches.
Currently, these distances vary from one and a half meters to the size of a chip (a few millimeters), and an auxiliary path of several meters along the cable introduces a long delay other than the direct transmission of the packet to the channel. The same can be said about the switching time.

Summary: For high-performance systems, a network that connects physically adjacent elements is more optimal, and such a network requires a switch with a minimal switching time. You can even enter a certain parameter equal to the ratio of the transmission delay with a direct connection or via a switch. We need an optimal solution for the switch with up to 10 inputs and a single-layer switching field (multiplexer, FIFO, demultiplexer).

Switch Structure
The receiving part consists of a standard link level with the stream fragmentation module (SSH_Synchronous Stream_Stream Fragmentation (2)) and FIFO of the physical channel buffer. FIFO is mandatory, and it is required to carry received symbols across the “clock” barrier. On the receiving part, the clock frequency is restored from the received data; on the switch side, this is the clock frequency of the switch core. It is at the input of this FIFO that the “Compensating Symbols” (SSH_Synchronous Stream_Slippage Effect (1)) are deleted from the received stream. This ensures a lower average rate when receiving symbols rather than the processing rate by the switch core.

User access to the network occurs through the modified receivers (transmitters), where the data link level is replaced with a user physical interface.

The switch core is a set of small modules, one for each virtual channel. The number of physical channels is relatively small, so each module (or a group of modules) can be switched to any of the available channels. Switching of such a module (group) occurs at the moment the virtual channel is created and does not change until it is deleted. A module, after being created (assigned) to its certain virtual channel (configured), begins to respond only to signals from a specific physical interface and to a specific address range (the same at the output). It should be noted that several modules can respond to the same address range (when receiving), which makes it possible to copy a stream and route it to several physical channels. Copying allows you to build not just linear routes, but broadcast ones for several recipients (tree circuit), one source - many recipients. In this case, each recipient will see the same symbol sequence (sequential consistency). The data being received can be service data (processed by the Switch CU) and user data (transmitted within the framework of the created virtual channels), determined by the least significant bit of a symbol.
Formation of the aggregate channel occurs approximately in the same way. The virtual channel buffer address is generated from the cyclic symbol counter. If the selected channel contains data, it is read and sent to the transmitter. If it is not available or an address does not belong to any buffer, the availability of data in the Switch CU module is requested. If it is not available, the data from the asynchronous data transmission module is requested. If it is not available, no data symbol is transmitted. On the receiving side, the processing unit (Virtual Channel Buffer, Switch CU, Asynchronous Data Unit) is determined by the symbol type. If an address belongs to the asynchronous channel buffer, but the symbol type is incorrect (service one), no entry is made to FIFO.
If an erroneous symbol is received (the receiver was unable to restore a symbol from the received signal), it is replaced with an “error” service symbol. Then this symbol is transmitted in the virtual channel. When receiving data from a virtual channel, you can request retransmission of only this symbol to recover the data.

Closing (deleting) a virtual channel occurs when a user symbol is read from FIFO - “a signal to close a channel”; after reading it (towards the transmitter), the virtual channel module is reset to an inactive state (until it is initialized by the Switch CU).
The principles of organizing asynchronous transmission, functioning of the control unit, and the algorithm for creating a virtual channel will be described in the following articles.

Topics for R&D:
1. Synchronous switch unit is quite transparent, and at this stage it is the structure that needs to be worked out, without implementing the CU and Asynchronous Data Unit. The interface for initializing the virtual channel modules must provide complete initialization in one clock cycle.